## Slide 1
Model Update and Curtailment Analysis Deep Dive
Prescient PCM vs Paper UC | TX-123BT | March 2026
Goal: update model-comparison interpretation and integrate curtailment-sweep results.
Inputs: corrected model-comparison report + curtailment notebook exports.
Output: prioritized benchmark actions and decision points.
Notes: Sources: /Users/yilu/Documents/GitHub/idaes-gtep/quality_reports/reports/model_comparison_prescient_vs_paper_uc_2026-02-28.md; /Users/yilu/Documents/GitHub/idaes-gtep/quality_reports/reports/curtailment_penalty_experiment_setup_2026-02-28.md; /Users/yilu/Documents/GitHub/idaes-gtep/gtep/pcm_analysis/curtailment_penalty_benchmark_summary.csv; /Users/yilu/Documents/GitHub/idaes-gtep/gtep/pcm_analysis/prescient_lmp_analysis_curtailment_penalty.ipynb

## Slide 2
What Changed Since Last Update
Accuracy-review corrections now integrated
Paper curtailment mechanism corrected: bounded net-load slack, no direct curtailment objective term.
Solver caveat added: paper shared code uses CONOPT path (continuous relaxation risk).
DA-first LMP convention enforced for summarizer (`LMP DA` fallback to `LMP`).
Load-weighted LMP metric added for system-level reporting consistency.
Notes: Sources: /Users/yilu/Documents/GitHub/idaes-gtep/quality_reports/reports/model_comparison_prescient_vs_paper_uc_2026-02-28.md; /Users/yilu/Documents/GitHub/idaes-gtep/quality_reports/reports/curtailment_penalty_experiment_setup_2026-02-28.md; /Users/yilu/Documents/GitHub/idaes-gtep/gtep/pcm_analysis/curtailment_penalty_benchmark_summary.csv; /Users/yilu/Documents/GitHub/idaes-gtep/gtep/pcm_analysis/prescient_lmp_analysis_curtailment_penalty.ipynb

## Slide 3
Highest-Impact Model Differences
From current model-comparison ranking
Rank | Difference | Impact | Confidence
1 | Renewable representation (net-load vs explicit renewable units) | Very high | High
2 | Curtailment treatment/economics | Very high | High
3 | Chronology/horizon (daily independent vs 90 sequential days with 36h RUC look-ahead) | High | High
4 | Pricing workflow (paper two-pass dual vs Prescient engine) | High | Medium-High
5 | Solver choice (CONOPT NLP relaxation vs Gurobi MILP) | Medium-High | High
Structural assumptions remain dominant; cap tuning alone is insufficient.
Notes: Sources: /Users/yilu/Documents/GitHub/idaes-gtep/quality_reports/reports/model_comparison_prescient_vs_paper_uc_2026-02-28.md; /Users/yilu/Documents/GitHub/idaes-gtep/quality_reports/reports/curtailment_penalty_experiment_setup_2026-02-28.md; /Users/yilu/Documents/GitHub/idaes-gtep/gtep/pcm_analysis/curtailment_penalty_benchmark_summary.csv; /Users/yilu/Documents/GitHub/idaes-gtep/gtep/pcm_analysis/prescient_lmp_analysis_curtailment_penalty.ipynb

## Slide 4
Paper Curtailment Mechanism (Corrected)
Code-backed interpretation
Wind/solar are subtracted from demand first to form net load (`load_b_t`).
`rnwcur_b_t` is a nonnegative slack on nodal balance.
If net load >= 0, `rnwcur_b_t = 0`; if net load < 0, `rnwcur_b_t <= -load_b_t/BaseMVA`.
Objective excludes direct curtailment cost term.
Meaning: paper curtailment is balancing relief, not explicit renewable market-bid economics.
Notes: Sources: /Users/yilu/Documents/GitHub/idaes-gtep/quality_reports/reports/model_comparison_prescient_vs_paper_uc_2026-02-28.md; /Users/yilu/Documents/GitHub/idaes-gtep/quality_reports/reports/curtailment_penalty_experiment_setup_2026-02-28.md; /Users/yilu/Documents/GitHub/idaes-gtep/gtep/pcm_analysis/curtailment_penalty_benchmark_summary.csv; /Users/yilu/Documents/GitHub/idaes-gtep/gtep/pcm_analysis/prescient_lmp_analysis_curtailment_penalty.ipynb

## Slide 5
Our Prescient Curtailment Realization
Threshold-proxy mechanism
Current pipeline does not expose a single standalone renewable-curtailment penalty switch.
Curtailment behavior emerges from SCED/RUC with configured threshold penalties.
Tracked outputs: `renewables_detail.csv` (`Curtailment`), `hourly_summary.csv` (`RenewablesCurtailment`).
Interpretation: this sweep is a diagnostic proxy of economics, not a structural reformulation.
Notes: Sources: /Users/yilu/Documents/GitHub/idaes-gtep/quality_reports/reports/model_comparison_prescient_vs_paper_uc_2026-02-28.md; /Users/yilu/Documents/GitHub/idaes-gtep/quality_reports/reports/curtailment_penalty_experiment_setup_2026-02-28.md; /Users/yilu/Documents/GitHub/idaes-gtep/gtep/pcm_analysis/curtailment_penalty_benchmark_summary.csv; /Users/yilu/Documents/GitHub/idaes-gtep/gtep/pcm_analysis/prescient_lmp_analysis_curtailment_penalty.ipynb

## Slide 6
Curtailment Sweep Setup
Case design and corrected baseline caveat
Penalty ($/MWh)
300
1000
2000
5000
10000
`penalty_1000` is not identical to historical baseline thresholds.
Uniform-threshold benchmark set is designed for clean sensitivity, not 1:1 baseline reproduction.
Common comparison window: 2019-01-01 00:00:00 to 2019-03-31 23:00:00
Notes: Sources: /Users/yilu/Documents/GitHub/idaes-gtep/quality_reports/reports/model_comparison_prescient_vs_paper_uc_2026-02-28.md; /Users/yilu/Documents/GitHub/idaes-gtep/quality_reports/reports/curtailment_penalty_experiment_setup_2026-02-28.md; /Users/yilu/Documents/GitHub/idaes-gtep/gtep/pcm_analysis/curtailment_penalty_benchmark_summary.csv; /Users/yilu/Documents/GitHub/idaes-gtep/gtep/pcm_analysis/prescient_lmp_analysis_curtailment_penalty.ipynb

## Slide 7
Curtailment Results Table
Core metrics from notebook exports
Case | Penalty | Neg LMP % | Floor-hit % | Weighted LMP | Curtailment MWh | OverGen MWh
penalty_300 | 300 | 9.62% | 1.52% | 9.79 | 118560 | 888328
penalty_1000 | 1000 | 10.51% | 1.50% | 3.96 | 124325 | 889003
penalty_2000 | 2000 | 11.43% | 1.51% | -7.91 | 125040 | 888986
penalty_5000 | 5000 | 11.91% | 1.49% | -39.57 | 121351 | 889607
penalty_10000 | 10000 | 12.80% | 1.49% | -88.35 | 123328 | 888693
Notes: Sources: /Users/yilu/Documents/GitHub/idaes-gtep/quality_reports/reports/model_comparison_prescient_vs_paper_uc_2026-02-28.md; /Users/yilu/Documents/GitHub/idaes-gtep/quality_reports/reports/curtailment_penalty_experiment_setup_2026-02-28.md; /Users/yilu/Documents/GitHub/idaes-gtep/gtep/pcm_analysis/curtailment_penalty_benchmark_summary.csv; /Users/yilu/Documents/GitHub/idaes-gtep/gtep/pcm_analysis/prescient_lmp_analysis_curtailment_penalty.ipynb

## Slide 8
Trend Interpretation
What the sweep says technically
Neg LMP share increases from 9.62% (penalty 300) to 12.80% (penalty 10000).
Floor-hit share stays ~1.5% across cases, indicating persistent clipping behavior.
Weighted LMP declines from 9.79 to -88.35 $/MWh.
Overgeneration remains high and nearly flat (~888-890 GWh), so structural surplus persists.
Notes: Sources: /Users/yilu/Documents/GitHub/idaes-gtep/quality_reports/reports/model_comparison_prescient_vs_paper_uc_2026-02-28.md; /Users/yilu/Documents/GitHub/idaes-gtep/quality_reports/reports/curtailment_penalty_experiment_setup_2026-02-28.md; /Users/yilu/Documents/GitHub/idaes-gtep/gtep/pcm_analysis/curtailment_penalty_benchmark_summary.csv; /Users/yilu/Documents/GitHub/idaes-gtep/gtep/pcm_analysis/prescient_lmp_analysis_curtailment_penalty.ipynb

## Slide 9
Benchmark Implications
What cap tuning can and cannot solve
Cap tuning is a useful diagnostic, not a full benchmark-alignment solution.
Persistent negative-price behavior points to formulation mismatch, not only threshold settings.
Primary levers remain: renewable representation, chronology coupling, and pricing workflow.
Notes: Sources: /Users/yilu/Documents/GitHub/idaes-gtep/quality_reports/reports/model_comparison_prescient_vs_paper_uc_2026-02-28.md; /Users/yilu/Documents/GitHub/idaes-gtep/quality_reports/reports/curtailment_penalty_experiment_setup_2026-02-28.md; /Users/yilu/Documents/GitHub/idaes-gtep/gtep/pcm_analysis/curtailment_penalty_benchmark_summary.csv; /Users/yilu/Documents/GitHub/idaes-gtep/gtep/pcm_analysis/prescient_lmp_analysis_curtailment_penalty.ipynb

## Slide 10
Action Plan and Decision Points
Next execution sequence
1. Approve paper-like benchmark mode for renewables/net-load treatment.
2. Keep curtailment sweep as diagnostics; do not treat it as structural equivalence.
3. Run day-isolated benchmark window (e.g., Day110) for sign/trend alignment check.
4. Define acceptance criteria: sign/trend first, magnitude second.
Notes: Sources: /Users/yilu/Documents/GitHub/idaes-gtep/quality_reports/reports/model_comparison_prescient_vs_paper_uc_2026-02-28.md; /Users/yilu/Documents/GitHub/idaes-gtep/quality_reports/reports/curtailment_penalty_experiment_setup_2026-02-28.md; /Users/yilu/Documents/GitHub/idaes-gtep/gtep/pcm_analysis/curtailment_penalty_benchmark_summary.csv; /Users/yilu/Documents/GitHub/idaes-gtep/gtep/pcm_analysis/prescient_lmp_analysis_curtailment_penalty.ipynb