## Slide 1
Prescient PCM vs Paper UC: Benchmarking Status and Effort
TX-123BT ERCOT | Collaborator/Supervisor Update | March 2026
Purpose: estimate effort needed to align Prescient PCM with paper UC benchmark.
Coverage: model-difference audit, curtailment experiment status, hydro Q1 benchmark signal.
Decision focus: where to invest benchmarking effort next.
IDAES-GTEP | Benchmarking update section (~20 minutes)

## Slide 2
Updates
Comparing paper’s pyomo and our PCM, main differences are renewable treatment, chronology, pricing workflow.
[update] Hydro inclusion in Q1 did not materially improve alignment to paper behavior.
[update] I updated curtailment implementation and redo a Q1, it is still running after 4 days.

## Slide 3
Paper UC vs Prescient PCM: Comparison Matrix
model comparison
Aspect | Paper model | Our Prescient
Renewables | Subtracted from load (net-load) | Explicit generators in clearing
Paper removed wind/solar from demand before optimization; Prescient keeps renewable units explicit in market clearing.

## Slide 4
Paper UC vs Prescient PCM: Comparison Matrix
model comparison
Aspect | Paper model | Our Prescient
Curtailment | Free relief variable in balance | Penalty/cap mediated behavior

## Slide 5
Paper UC vs Prescient PCM: Comparison Matrix
model comparison
Aspect | Paper model | Our Prescient
Pricing | Two-pass dual pricing; fixed commitment | Integrated RUC/SCED pricing
Notes: paper uses explicit fixed-commitment re-solve for dual prices; Prescient prices come from its integrated RUC/SCED market engine.

## Slide 6
Paper UC vs Prescient PCM: Comparison Matrix
model comparison
Aspect | Paper model | Our Prescient
Chronology | Daily independent runs | Rolling horizons (90d, look-ahead)

## Slide 7
Paper UC vs Prescient PCM: Comparison Matrix
model comparison
Aspect | Paper model | Our Prescient
Reserves | Custom reserve constraints | reserve_factor design

## Slide 8
Paper UC vs Prescient PCM: Comparison Matrix
model comparison
Aspect | Paper model | Our Prescient
Line ratings | Day-specific / hourly DLR options | RTS-GMLC path unless remapped

## Slide 9
Curtailment Penalty Work: Current Status
Experiment framework in place; run still in progress
Ongoing 4-day simulation for 90-day experiment; run not finished yet.
Experiment implemented in current Prescient pipeline and reproducible by case manifest.
This section intentionally remains brief until the full run is complete.
Penalty sweep ($/MWh)
300
1000
2000
5000
10000
How new curtailment was applied:
No "renewable curtailment penalty" option in PCM
Use threshold penalty as proxies to influence dispatch, curtailment, and lmp outcomes.
Notes: Source: /Users/yilu/Documents/GitHub/idaes-gtep/quality_reports/curtailment_penalty_experiment_setup_2026-02-28.md

## Slide 10
Hydro Q1 Check: No Material Improvement
Hydro inclusion does not uplift LMP alignment in current setup
Scenario | Weighted LMP | Floor-hit share | Min | Max
Hydro Btheta UC+ED | 8.33 | 1.07% | -1000.0 | 276.6
Hydro Btheta UC-only | 8.10 | 1.07% | -1000.0 | 276.2
No-hydro Benchmark Q1 | 8.26 | 1.07% | -1000.0 | 368.0
Hydro UC+ED and hydro UC-only results were very close to no-hydro Q1
Notes: Sources: /Users/yilu/Documents/GitHub/idaes-gtep/gtep/pcm_analysis/PCM_result_hydro_q1_comparison.json; /Users/yilu/Documents/GitHub/idaes-gtep/gtep/pcm_analysis/prescient_lmp_analysis_with_hydro_q1.ipynb

## Slide 11
Decisions points
Lock scope before deeper simulation spend
1. Prioritize structural alignment (renewables/chronology/pricing) before hydro expansion.
2. Define success criteria as sign/trend alignment first, magnitude second.
Notes: This closing slide is for meeting decisions and near-term execution commitments.